## Slide 1: PJ22045 1R8T Relay
AURORA RELAY · DESIGN REV 0.12
One RFSoC ADC stream, broadcast by a VU13P to eight RFSoC DACs over Aurora 64B66B
1 → 8 broadcast
2 × 25.625 Gb/s
40-bit timestamps
No FIFO loss

## Slide 2: One ADC stream, eight time-aligned DACs
GOALS
40.96
Gb/s of ADC samples carried on every link
8
DAC outputs fed from one z1 ADC channel
82.6 %
link load, 17 % headroom on 2 × 25.625 Gb/s
2.0 µs
default ADC → DAC latency (delay + 1 cycle)
Requirement | How the design meets it
1 ADC stream → 8 DACs (1R8T) | z1 X0Y1 core 1 → VU13P X1Y8 core 1 → broadcaster 1 → 8 → z2, one DAC per Aurora core
160-bit samples on 128-bit Aurora | header_insertion / header_extraction with a 64-bit header per 1024 samples
Output at the correct time | 40-bit timers on z1 and z2 started by one SYSREF; data_delay + data_aligner on z2
All links identical, no FIFO loss | same FIFO / slice per link; FIFO budget simulated with real depths

## Slide 3: One 47DR in, one VU13P, one 47DR out
ARCHITECTURE
TRANSMITTER · Z1
ZU47DR · z1
• ADC tile 0 ch 0, I/Q
• 160 b @ 256 MHz + 40-bit time
• Aurora X0Y1 core 1
• Other 7 ADCs loop back to own DAC
RELAY · BROADCAST
VU13P
• RX X1Y8 core 1 (quad 228)
• SLR crossing at 400 MHz
• Broadcaster 1 → 8, no tready
• TX X1Y4–X1Y7, cores 0 + 1
RECEIVER · Z2
ZU47DR · z2
• 8 Aurora cores X0Y1–X0Y4
• Extract 128 → 160 b + tuser
• Delay + align to z2 timer
• DAC s00 s02 s10 s12 s20 s22 s30 s32
1 link
8 links
Orange: the z1 ADC stream (one 2-lane Aurora). Blue: eight 2-lane Auroras to z2, all carrying the same samples. Every link: Aurora 64B66B, Framing, 2 × 25.625 Gb/s, 156.25 MHz refclk.

## Slide 4: Link plan: 8 Aurora cores per side
ARCHITECTURE
z1 quad (bank) | z1 lanes C0 / C1 | VU13P quad (bank) | VU13P lanes C0 / C1 | z2 quad | Use
X0Y1 (128) | X0Y4-5 / X0Y6-7 | X1Y8 (228) | X1Y32-33 / X1Y34-35 | — | ADC stream on core 1
X0Y2 (129) | X0Y8-9 / X0Y10-11 | X1Y9 (229) | X1Y36-37 / X1Y38-39 | — | link only
X0Y3 (130) | X0Y12-13 / X0Y14-15 | X1Y10 (230) | X1Y40-41 / X1Y42-43 | — | link only
X0Y4 (131) | X0Y16-17 / X0Y18-19 | X1Y11 (231) | X1Y44-45 / X1Y46-47 | — | link only
— | — | X1Y4 (224) | X1Y16-17 / X1Y18-19 | X0Y1 (128) | broadcast M00 / M01
— | — | X1Y5 (225) | X1Y20-21 / X1Y22-23 | X0Y2 (129) | broadcast M02 / M03
— | — | X1Y6 (226) | X1Y24-25 / X1Y26-27 | X0Y3 (130) | broadcast M04 / M05
— | — | X1Y7 (227) | X1Y28-29 / X1Y30-31 | X0Y4 (131) | broadcast M06 / M07
Reference clocks
VU13P AW9 AT11 AM11 AH11 AD11 Y11 T11 M11 · ZU47DR AA33 W33 U33 P31 (golden IBERT)
Not yet proven
Lane pairing C0↔C0 / C1↔C1 is assumed straight; IBERT confirms the quad pairing only

## Slide 5: How a sample travels from ADC to DAC
HOW IT WORKS
z1 · FPGA_clk 256 MHz
Aurora user_clk
VU13P · 400 MHz fabric
Aurora user_clk
z2 · FPGA_clk 256 MHz
RFDC ADC
m00 / m01
2 × 80 b
Combine
160 b
+ tuser time
Packetize
1024 / pkt
tlast
Header in
160 → 128 b
64 b header
RX FIFO
rx_fifo_c1
512
Broadcast
1 → 8
no tready
Header out
128 → 160 b
tuser = hdr+k
data_delay
due =
t + delay
FIFO 1024
hold until
due
Aligner
release
→ DAC
Aurora TX
X0Y1 C1
Aurora RX
X1Y8 C1
Aurora TX
8 cores
Aurora RX
z2 C0/C1
Time in the header
The 40-bit time of the first sample travels in the header; z2 adds the beat index
Same samples on 8 links
The broadcaster copies every 128-bit beat, header and tlast to all eight TX cores
Played at a fixed latency
Each z2 sample leaves when the z2 timer = its time + axi_delay

## Slide 6: Packet format: 160 b over 128 b
PROTOCOL
ip 16
type 8
time · 40 bits
samples 0 … 1023 · 1024 × 160 bits (5 I/Q pairs each)
header · 64 bits, once per packet
tlast on the last beat · Aurora Framing carries it over both hops
Field | Value
Sample | 160 b = {Q4,I4,…,Q0,I0}, 16 bit each
Rate | 1.28 GSPS complex = 256 MHz × 5
tuser (z1 and z2) | {24’b0, time[39:0]}
Packet | 64 + 1024 × 160 b = 1280.5 beats of 128 b
Overhead | header 0.04 % · ≈ 1282.5 link cycles / 4 µs
Recovered tuser | header time + beat index
Half beat carried over
A packet is 1280.5 beats; the half beat goes into the next packet, so packets depend on each other
Proposed: 1022 samples
64 + 1022 × 160 b = 1278 whole beats; a lost packet then costs only its own samples

## Slide 7: Each DAC plays at timestamp + delay
PROTOCOL
Requirements
• z1 and z2 FPGA_clk from one reference
• one SYSREF pulse seen by both boards
• release z2 arstn, then z1, then SYSREF
• delay > path latency
• delay − latency < ≈ 1000 cycles
100 ppm clock offset = 25 600 samples/s of drift: the z2 FIFO overflows in < 50 ms
1
Start First PL SYSREF after arstn sets start on both boards; both 40-bit timers count from 0.
t = 0
2
Stamp z1 tags each 160-bit sample with its timer value (tuser).
every clock
3
Carry The first time of each packet rides in the 64-bit header.
1 / 1024
4
Rebuild z2 header_extraction: tuser = header time + beat index.
per beat
5
Delay data_delay: due = time + axi_delay (0xA008_0000, default 512).
2.0 µs
6
Release data_aligner outputs the sample when the z2 timer = due; zeros before that.
delay + 1

## Slide 8: One time base: two timers, one SYSREF
TIME BASE
PL SYSREF
one pulse, both boards
z1 timer_1
0
1
2
3
4
5
…
T
stamps every sample: tuser = {24’b0, time}
z2 timer_1
0
1
2
3
4
5
…
T
drives all 8 data_aligners
start = 1 on the
next 256 MHz edge
Block | Function
timer_1 (timer.v) | 40-bit counter, +1 per FPGA_clk (3.906 ns) while start = 1
sync_pulse_to_level_1 | start = 1 on the first SYSREF after arstn, then stays 1
xpm_cdc_gen_1 | axi_gpio_arstn (0xA001_0000) → irstn on FPGA_clk
wrap | 2⁴⁰ counts = 71.6 min, same cycle on both boards
Start sequence
1 arstn = 0 on z1 and z2 (timers held at 0)
2 release z2, then z1
3 one PL SYSREF to both boards
→ both timers count from 0 in the same cycle

## Slide 9: Latency: T on z1 → T + delay + 1 on z2
TIME BASE
z1 stamps
T = 1000
header
time 0, index 1000
VU13P
forwards, no timer
z2 rebuilds
time = 1000
data_delay
due = 1512
FIFO
waits ≈ 500
aligner
DAC at 1513
Example with delay = 0x200 = 512: all eight z2 outputs release this sample in the same cycle, 513 × 3.906 ns = 2.004 µs after capture.
Quantity | Value (delay 512)
ADC → DAC latency | (delay + 1) × 3.906 ns = 2.004 µs
Samples held in z2 FIFO | delay − transport (sim: 504 / 1024)
Valid delay | transport < delay < transport + ≈ 1000
Late sample | sent at once (timing lost)
Wrap (71.6 min) | epoch bit in the aligner: no glitch
Event | Effect → recovery
Clocks not from one reference | timers drift → fix clock tree
Different SYSREF pulses | constant offset → restart
One board reset alone | z1: output stops · z2: unscheduled → restart
Lost packet / time jump | see open items → restart
delay lowered while running | output stops → change at arstn = 0
Restart = arstn 0 on both, release z2 then z1, one SYSREF. ILA probes per hier_rx: timestamp, sys_time, data_time, end_time.

## Slide 10: z1: ADC 00 out, seven loopbacks
ARCHITECTURE
ADC ch | Combiner | Destination
00 (I/Q) | axi_stream_combininp_adc00 | → S_AXIS_X0Y1_C1
02 | axi_stream_combininp_adc02 | DAC s02
10 | axi_stream_combininp_adc10 | DAC s10
12 | axi_stream_combininp_adc12 | DAC s12
20 | axi_stream_combininp_adc20 | DAC s20
22 | axi_stream_combininp_adc22 | DAC s22
30 | axi_stream_combininp_adc30 | DAC s30
32 | axi_stream_combininp_adc32 | DAC s32
Link path
• axis_packetizer_0 → S_AXIS_X0Y1_C1
• tx_c1: cdc_fifo 16 → header_insertion → out_fifo 16
• aurora_x0y1_1 · lanes X0Y6-7
Removed
PARAM_RECORDER, phase_calibration, pulse generator, debug VIOs; DAC s00 and Aurora RX unused
RFDC: 3.84 GSPS, ×3 decimation, NCO +0.84 GHz; the combiner’s interleaved I/Q word is the format the DAC expects.

## Slide 11: VU13P: receive once, send eight times
ARCHITECTURE
hier_x1y8
Aurora core 1 RX
quad 228
link_x1y8
rx_slice_c1 →
rx_fifo_c1 512
axis_slr_x1y8_to_tx
Multi-SLR
crossing
axis_broadcaster_0
1 → 8
no tready
link_x1y4..7
tx_fifo_c0/c1 512
→ tx_slice (SLR)
hier_x1y4..7
8 Aurora TX
quads 224–227
user_clk (quad 228) → axis_aclk 400 MHz (clk_wiz_0) → user_clk (quads 224–227)
Uniform links
Every quad X1Y4…X1Y11: hier_x1yN (2 cores) + an identical link_x1yN
Independent outputs
No back-pressure from the broadcaster: a stalled or down z2 link only loses its own data
Fast enough
Fabric 128 b × 400 MHz = 51.2 Gb/s, above the 49.7 Gb/s link: the RX FIFO never fills
Also kept: the 13P↔13P link (X0Y11 / X0Y13), not part of the 1R8T path.

## Slide 12: z2: eight links, eight DACs
ARCHITECTURE
Container port | hier_rx | DAC
M_AXIS_X0Y1_C0 / C1 | hier_rx_x0y1 | s10 / s12
M_AXIS_X0Y2_C0 / C1 | hier_rx_x0y2 | s00 / s02
M_AXIS_X0Y3_C0 / C1 | hier_rx_x0y3 | s20 / s22
M_AXIS_X0Y4_C0 / C1 | hier_rx_x0y4 | s30 / s32
AXI peripheral | Address
DMA_Ctrl | 0xA000_0000
axi_gpio_arstn | 0xA001_0000
axi_gpio_pma_rst | 0xA002_0000
axi_intc_0 | 0xA003_0000
usp_rf_data_converter_1 | 0xA004_0000 (256 K)
axi_delay | 0xA008_0000
Per core in hier_rx_x0yN
• data_delay → axis_data_fifo (1024) → data_aligner
• ILAs on data_time, sys_time, end_time
• DAC tile 3 configured like tile 2
axi_delay
• 32-bit AXI GPIO, default 0x200 = 512 cycles
• drives the delay of all four hier_rx
• reset by irstn: release arstn before writing

## Slide 13: Every name follows the connectivity
VIVADO
Level | Name | Example
GT ports | GT_SERIAL_TX/RX_<QUAD>_C<n> | GT_SERIAL_TX_X0Y1_C1
Container data ports | S_AXIS_<QUAD>_C<n> → core n TX · M_AXIS_<QUAD>_C<n> ← core n RX | M_AXIS_X1Y8_C1
Quad hierarchy pins | GT_SERIAL_TX/RX_C<n>, S_AXIS_TX_C<n>, M_AXIS_RX_C<n>, GT_REFCLK, arstn_c<n> | hier_x1y4/GT_REFCLK
TX / RX / link pins | S/M_AXIS_TX_C<n>, S/M_AXIS_RX_C<n>, user_clk, axis_aclk, arstn_c<n> | link_x1y8/M_AXIS_RX_C1
Cells | tx_c<n>, rx_c<n>, tx_fifo_c<n>, rx_slice_c<n>, user_rst_sync_c<n> | link_x1y4/tx_fifo_c0
Wires | driver name <cell>_<pin> | rx_fifo_c1_M_AXIS
RF ports | converter pin | vout02 = DAC tile 0 ch 2
Misleading names removed
S_AXIS_X0Y1 fed core 1 · every VU13P refclk pin was gt_x1y8_diff_ref · wires named after other quads · vout01 was DAC ch 2
Checked
144/144 ports match their traced core · net counts unchanged · all BDs validate · XDC ports present

## Slide 14: Link load 82.6 %, 17 % headroom
PERFORMANCE
Chart: Link cycles per packet time (4 µs)
| ADC samples | Header + framing | Headroom
Link cycles per 4 µs | 1280 | 2.5 | 270.5
Step | Value
ADC payload | 160 b × 256 MHz = 40.96 Gb/s
Header | 64 b per 1024 samples = +0.04 %
Per packet on the link | 1280.5 beats + separator + stall ≈ 1282.5 cycles
Link payload capacity | 2 × 25.625 Gb/s × 64/66 = 49.7 Gb/s
Link utilisation | ≈ 82.6 %
VU13P fabric | 128 b × 400 MHz = 51.2 Gb/s
End-to-end latency | delay + 1 cycles (default 2.0 µs)
Clock compensation (≈ 0.06 %) and the 64b/66b gearbox pause are inside the 49.7 Gb/s figure. The doughnut counts one 4 µs packet time.

## Slide 15: FIFOs: no loss up to a 1.6 µs stall
PERFORMANCE
FIFO | Depth | Normal | 1 µs stall | 3 µs stall
z1 tx_c1/cdc_fifo * | 16 | 1 | 1 | 1
z1 tx_c1/out_fifo | 16 | 4 | 4 | 4
VU13P rx_fifo_c1 * | 512 | 1 | 1 | 1
VU13P tx_fifo_c<n> * | 512 | 4 | 321 | 512 · loss
z2 rx_c<n>/in_fifo * | 512 | 1 | 1 | 1
z2 rx_c<n>/cdc_fifo | 512 | 6 | 259 | 411
z2 hier_rx FIFO * | 1024 | 504 | 504 | 1024 · loss
* upstream ignores tready (RFDC, Aurora RX, broadcaster, data_delay): a full FIFO here loses data
Normal: no loss
Every FIFO stays near empty; the hold FIFO keeps exactly the delay (504)
1 µs stall: no loss
VU13P TX peaks at 321/512, z2 latency stays constant
3 µs stall: loss
TX FIFO overflows, that z2 output breaks until reset
Simulated with real RTL and depths, Aurora gearbox / clock-compensation / frame-separator pauses and independent clocks (scripts/sim_chain/run_fifo.sh).

## Slide 16: Simulation confirms exact timing
VERIFICATION
Test | Result | Status
End-to-end, delay 512 and 200 | every sample at the DAC exactly delay + 1 cycles after its z1 timestamp | PASS
40-bit timer wrap (71.6 min) | latency constant through 0xFF_FFFF_FFFF → 0 | PASS
FIFO budget, normal and 1 µs stall | no loss, peak 321 / 512 | PASS
Block designs (all 3 projects) | validate clean after the naming pass | PASS
RFDC configuration | z1 ADC and z2 DAC: 3.84 GSPS, ×3, NCO ±0.84 GHz | PASS
delay 1400 | hold FIFO overflow (expected: limit §6.7) | LIMIT
1 lost packet | word misalignment until reset; OK with 1022 samples / packet | OPEN
2 lost packets | data_delay guard freezes the time until reset | OPEN
scripts/sim_chain/run.sh <delay> [wrap] [lost_packets] [packet_length] · real RTL of packetizer, header insertion/extraction, data_delay, data_aligner, timer.

## Slide 17: All three bitstreams meet timing
IMPLEMENTATION
+0.011
ns setup slack · VU13P relay
+0.008
ns setup slack · z1 (47dr1)
+0.023
ns setup slack · z2 (47dr2)
0
failing endpoints; hold +0.010 ns on all three
 | VU13P · relay | z1 · 47dr1 | z2 · 47dr2
GT / refclk placement | 40 GTs X1Y16–47 (+13P↔13P) · refclks = golden | 16 GTs X0Y4–19 · = golden | 16 GTs X0Y4–19 · = golden
LUT / FF / BRAM | 3.3 % / 4.7 % / 18.4 % | 14.7 % / 10.1 % / 20.8 % | 21.3 % / 16.1 % / 46.9 %
DRC / methodology | warnings · TIMING-4/27 (inherited clk_wiz) | warnings only | warnings only
Outputs | aurora_gty_vu13p_rst_wrapper.bit + .ltx | design_1_wrapper.bit + .ltx | design_1_wrapper.bit + .ltx
Vivado 2025.2 with debug ILAs. VU13P: build #6 (rev 0.12, core-1 reset fix D19; was +0.025 ns in build #5), GT placement unchanged. z1 / z2: build #5 (rev 0.11). Release: PJ22045_1R8T_release_rev0.12_20261014.tar.gz.

## Slide 18: An ILA on every hop of the stream
DEBUG
Board | ILA | Clock | Slots | Use
z1 | system_ila_1 | FPGA_clk 256 MHz | ADC combiner · packetizer (tuser) | samples + timestamps before the link
z1 / z2 | ila_x0y1 … ila_x0y4 | quad user_clk | TX C0/C1 · RX C0/C1 (2048 deep) | z1 ADC stream = ila_x0y1 TX C1
VU13P | ila_x1y4 … ila_x1y11 | quad user_clk | TX C0/C1 · RX C0/C1 (2048 deep) | received stream = ila_x1y8 RX C1
VU13P | ila_bcast | axis_aclk 400 MHz | broadcaster in + M00…M07 | tready = 0 → that link's TX FIFO full
z2 | hier_rx_x0yN/system_ila_0/1 | FPGA_clk | delay · FIFO · aligner + times | release at sys_time = data_time
Follow one packet
Trigger on tlast: z1 ila_x0y1 → VU13P ila_x1y8 → ila_bcast → ila_x1y4..7 → z2 ila_x0yN → hier_rx ILAs; the header beat carries the time
Always running
ILA resets are left open, so they keep capturing while a link is down (link-loss debugging). Load each bitstream with its own .ltx

## Slide 19: Core-1 link reset fixed on the VU13P
REV 0.12 · D19
8 / 8
quads rewired and checked in the built netlist
+0.011
ns setup slack after the rebuild (hold +0.010)
= golden
GT and refclk placement unchanged

## Slide 20: Three documents, full detail
DOCUMENTS
DOCS/DESIGN.DOCX
DESIGN
• System design, requirements, decisions D1–D20
• Bring-up, ILAs, release
• 18 figures
DOCS/…DOCX
SIGNAL_TRANSMISSION
• Every block on the path, RTL and IP configuration
• Links, flow control, FIFOs, start-up, errors
• 13 figures
DOCS/…DOCX
TIMING_SYNC
• Time base, SYSREF, stamping, rebuild
• data_delay / data_aligner cycle by cycle
• Latency, alignment, failure modes
• 8 figures

## Slide 21: Packet loss needs a reset: 3 fixes
OPEN ITEMS
ALIGNMENT
P1 · 1022 samples
• Packet = 1278 whole beats
• A lost packet costs only its samples
• Verified in simulation
TIMESTAMPS
P2 · resync guard
• data_delay freezes on a jump > delay + 1024
• Resync on the next header instead
PROCEDURE
P3 · bring-up order
• links up → z2 arstn → z1 arstn → SYSREF
• repeat after any link drop
Also
• Common reference for z1/z2 FPGA_clk and one shared SYSREF are mandatory; PL_SYSREF capture is not timed (D20, check on hardware)
• Lowering axi_delay or resetting one board while running stops or unschedules the output: change delay only in reset
• Clean-ups: data_delay.v tuser slice, clk_wiz TIMING-4/27 (inherited)

## Slide 22: Bring up three boards
NEXT STEPS
1
Bitstreams built and timing-clean: <proj>.runs/impl_1/*.bit + .ltx (rebuild: run_build.sh <proj>)
2
Program VU13P, then z1 and z2, each with its own .bit + .ltx
3
Links channel_up on the core-status VIOs: VU13P X1Y8 C1 and X1Y4–X1Y7, z2 X0Y1–X0Y4
4
Delay write axi_delay (0xA008_0000) on z2; default 0x200 = 2 µs
5
Start release arstn on z2, then z1; one SYSREF to both boards
6
Check ILAs: start offset z1 ↔ z2 = 0, transport latency, release at sys_time = data_time, no gaps